## Slide 1: Fireball data analysis summary

## Slide 2: Transverse instabilities
Diagnostic:
Chromox screens before and after cell
Data format:
NXN array (x (mm) and y (mm) on x and y axes)
Data processing:
Background subtraction
Subtract darkfield image
Subtract images (5) with no plasma and no beam
Analysis
Integrate over x to see intensity vs y, and vice versa.
Compute standard deviation of spot in x and y
Data plotting:
Compare pair beam & plasma to shots with pair beam and no plasma
Show raw image (with and without bkg subtraction)
Show lineouts (mean and error over 5 shots) and standard deviation of spot in x and y (screen after cell).
Hope to see a smaller beam with plasma.
Stretch goal: If we see focusing with plasma - useful to plot std of centroid averaged over 5 shots at several different plasma densities to track how spot size changes with plasma density.

## Slide 3: Longitudinal instabilities: timing
Diagnostic:
Streak optical transition radiation produced when pairs pass through metal foil.
Data format:
NXN array: time (ps) on y axis, and space (mm) on x axis.
For timing the streak camera to the signal from the beam:
Plasma OFF & Target in (pairs, no plasma)
Data processing:
Background subtraction
Subtract darkfield image
Subtract images (5) with plasma and no beam
Analysis
Total counts single shot
Total counts averaged over five shots
Data plotting:
Streak in focus mode (no time resolution)
Compare shots with beam and no plasma to shots with no beam and no plasma
Show raw image (with and without bkg subtraction)
Total counts (single shots and/or mean & error over n shots)
Streak in sweep mode (with time resolution)
Total counts single shot or averaged over n shots vs time delay – most likely input by user or hardcoded
Hope to see signal above background

## Slide 4: Longitudinal instabilities: looking at instabilities (data)
Diagnostic:
Streak optical transition radiation produced when pairs pass through metal foil.
Data format:
NXN array: time (ps) on y axis, and space (mm) on x axis.
For looking at instabilities:
Data processing:
Background subtraction
Subtract darkfield image
Subtract (n) images with plasma and no beam
Analysis
Integrate over x to see intensity vs time, and vice versa
Fast Fourier transform (FFT) intensity vs time
Data plotting:
Compare shots with pair beam & plasma to shots with pair beam and no plasma
Show raw image (with and without bkg subtraction)
Show traces of intensity vs time (mean and error over n shots). Also useful to have intensity vs x to check focusing.
Hope to see modulations in intensity at the plasma frequency
Stretch goal: If we see intensity modulations- useful to plot modulation scale length (from FFT) at several different plasma densities to track how spot size changes with plasma density. Also useful to plot contrast of density modulations (max-min)/(max+min) – this is proportional to the amplitude of the plasma waves.

## Slide 5: Synchrotron emission: timing
Diagnostic:
Gated spectrometer
Data format:
NXN array: space on y axis, and wavelength (mm) on x axis.
For timing the gated spectrometer to the signal from the beam – use OTR:
Plasma OFF & Target in (pairs, no plasma)
Data processing:
Background subtraction
Subtract darkfield image
Subtract (n) images with plasma and no beam
Analysis
Total counts single shot and averaged over five shots
Data plotting:
Start spectrometer with ms gate
For a shot with beam and no plasma compared to a shot with no beam and no plasma:
Show raw image (with and without bkg subtraction)
Total counts (single shot or averaged over multiple shots with error)
Decrease gate iteratively to 2ns
Show raw image (with and without bkg subtraction)
Total counts single shot, or averaged over n shots vs time delay (input by user/hardcoded)
Hope to see signal above background

## Slide 6: Synchrotron emission: looking at instabilities (data)
Diagnostic:
Gated spectrometer
Data format:
NXN array: space on y axis, and wavelength (mm) on x axis.
For looking at instabilities:
Data processing:
Background subtraction
Subtract darkfield image
Subtract (n) images with plasma and no beam
Subtract (n) images with no plasma and with beam
Analysis (with plasma & beam)
Integrate over y to see intensity vs wavelength, and vice versa.
Total counts (single shot & averaged over n shots)
Data plotting:
Compare shots with pair beam & plasma to shots with pair beam and no plasma, and to shots with plasma and no pair beam.
Show raw image (with and without bkg subtraction)
Compare total counts (single shot & averaged over n shots with error)
Stretch goal: If we see signal above background, we want to compare the total signal above background averaged over five shots for different runs. We will insert different polarizing filters into the beam on different runs. Comparing the intensity on each run tells us how polarized the signal is in each orientation.

## Slide 7: Magnetic field: Faraday diagnostic
Diagnostic:
Laser coupled into oscilloscope (via fast diode or similar?)
Data format:
2XN array: time (ps) along x axis, and voltage (V) along y axis.
For looking at instabilities:
Data processing:
Background subtraction
Subtract (n) images with no plasma and with beam
Subtract reference trace (from the laser that doesn’t pass through the plasma: although this may be done already in the set-up itself – best to check with Jack)
Analysis (with plasma & beam)
Compute delay factor due to cables etc
Average trace over multiple shots: get mean and std
Data plotting:
Compare shots with pair beam & plasma to shots with pair beam and no plasma, and to shots with proton beam only and no plasma
Show voltage vs time traces (single shot and averaged over n shots with error)
Hope to see oscillating time-varying signal for shots with plasma

## Slide 8: Magnetic field: B-dot probes
Diagnostic:
4 loops of copper wire. Two loops are mounted 1m into the cell – one transverse to beam, one parallel to beam. Then two more loops after 3m of plasma (at end of cell). These are also oriented orthogonally to each other (b dot orientation determines whether is measures the b fields longitudinally or transversely to the beam propagation direction).
Data format:
2XN array: time (ps) along x axis, and voltage (V) along y axis.
For looking at instabilities:
Data processing:
Background subtraction
Subtract reference (5) with no plasma and with beam
Analysis (with plasma & beam)
Compute delay factor due to cables etc
Average trace over multiple shots: get mean and std
Data plotting:
Compare shots with pair beam & plasma to shots with pair beam and no plasma, and to shots with proton beam only and no plasma. We also want to compare the two orthogonal b dot signals to each other and the two longitudinal b dots to each other: this tells us how much the b field grows after 1m and 3m of plasma. We want to compare the two orthogonally oriented b-dots after 1 m of plasma, and then the other two after 3m of plasma: this may tell us about the competition between the transverse and longitudinal instabilities.
Show voltage vs time traces
Hope to see oscillating time-varying signal (single shot and averaged over n shots with error) with plasma, increasing in voltage with increasing distance of the beam in the plasma, for both the longitudinal and the transverse b-dots.

## Slide 9: Pair spectrometer
Diagnostic:
Chromox screens either side of beam axis, imaged by cameras (upstream) with telescopic lenses. An electromagnet disperses the pair beam transversely, imprinting energy along the x-axis
Data format:
NXN array: space (mm) y axis, and space (mm) on x axis. A particle tracking code can be used convert the x axis units from mm to MeV. Using the distance from the screens to the target, the y-axis can be converted to beam divergence (theta (mrad) = x[mm]/z[m]=px [mm]/pz[m])
For looking at instabilities:
Data processing:
Background subtraction
Subtract darkfield image
Analysis
Integrate over x (to get divergence vs charge)
Integrate over y (to get energy vs charge)
Compute std divergence
Data plotting:
Compare shots with beam no plasma to shots with beam and plasma
Show raw image (with and without bkg subtraction)
Plot spectrum vs counts on camera (proportional to charge) (electrons & positrons): (single shot and averaged over n shots with error)
Plot divergence counts on camera (proportional to charge) ) (electrons & positrons): (single shot and averaged over n shots with error)
Plot std of beam divergence for single shot and/or averaged over n shots with error.
Hope to see difference in beam divergence with and without plasma, and hopefully also differences in electron and positron beam divergence
If we’re really lucky, we might see evidence of electron and/or positron acceleration (different spectrum with plasma compared to without: some particle will have more energy and some will have less, depending on where they are in the beam, longitudinally.)